## Slide 1: Introduksjon til informasjonsmodellering
TVB4100 Informasjonsstrukturering for BAE
Knut Jetlund, NTNU i Gjøvik
knut.jetlund@ntnu.no
August 2023

## Slide 2: Hensikt
Etter å ha gjennomgått fagstoffet skal du kunne
  forstå de grunnleggende elementene for modellering av virkeligheten i konseptuelle informasjonsmodeller

## Slide 3: Litteraturhenvisninger
PhD Knut Jetlund
  Kap. 2
SOSI del 1 Generell del: Regler for UML-modellering – Versjon 5.1
  Kap. 10
Noy & McGuinness. Ontology Development 101: A Guide to Creating Your First Ontology. 2001
Schenck & Wilson, Information modelling : The EXPRESS way. 1994

## Slide 4: Det finnes en virkelig verden der ute
Konseptuelle modeller definerer objekttyper, egenskaper, tillatte verdier og sammenhenger
Notes: Liker å starte med den ubehagelige sannheten for oss som jobber med datamodeller. Det finnes en virkelig verden der ute, det er ikke det vi har i datamaskinene som er virkeligheten. Vår jobb er å lage best mulig digital representasjon av de virkelige vegene, skilt, tunneller, rekkverk, kummer osv.

## Slide 5: Standardisering og informasjonsmodeller Motivasjon og verdi
https://www.veier24.no/artikler/fikk-25-millioner-for-trobbel-med-stikningsdata-og-vegmodeller/456614

## Slide 6: https://www.tek.no/artikler/tesla-version-9-har-endelig-kommet-til-norge/449798

## Slide 7
The most detailed maps of the world will be for cars, not humans | Ars Technica (netblogpro.com)

## Slide 8: https://www.fool.com/investing/2018/09/06/self-driving-cars-understanding-6-autonomous-level.aspx

## Slide 9
The Crucial Differences Between AV Maps and HD Maps | Mobileye Blog

## Slide 10: Samspillet mellom aktører
The SEMIC Style Guide for Semantic Engineers :: SEMIC (semiceu.github.io)

## Slide 11: DIKW: Data, Information, Knowledge, Wisdom
90
2
Fartsgrense 90 km/t
Temperatur på vegen 2 grader Celcius
Kan kjøre 90 km/t lovlig
Bør redusere farten pga fare for glatt veg ved temperatur nær frysepunktet
Menneskelig intuisjon, erfaring bruk i nye kontekster

## Slide 12: DIKW - Data, Information, Knowledge and Wisdom
The DIKW Hierarchy. Adapted from (Rowley, 2007).
Notes: The hierarchy of Data, Information, Knowledge and Wisdom has been described as a pyramid, where data is at the lower level, followed by information and knowledge, and wisdom at the pinnacle. Each level of the hierarchy, starting from the top, relies on the level below: wisdom is gained from knowledge; knowledge is gained from information; information is gained from data.
Data are simple symbols. For example, the numbers «90» or «2».
Information is data put into context, where it has a meaning. For example, the speed limit 90 km/h or outdoors temperature 2 degrees Celcius.
Knowledge is gained by combining information. For example, a vehicle can know that it is allowed to drive at 90 km/h according to the speed limit, but also that it should reduce the speed due to possible challenging conditions because the outdoors temperature is 2 degrees.
The final level, wisdom, has been described as a purely human state. With wisdom, we are able to plan for the future and apply knowledge to new situations.

## Slide 13: Det finnes en virkelig verden der ute
Konseptuelle modeller definerer objekttyper, egenskaper, tillatte verdier og sammenhenger
A conceptual model, …, is an abstract representation of a system and comprises well-defined concepts, their qualities or attributes, and their relationships to other concepts.
Notes: Liker å starte med den ubehagelige sannheten for oss som jobber med datamodeller. Det finnes en virkelig verden der ute, det er ikke det vi har i datamaskinene som er virkeligheten. Vår jobb er å lage best mulig digital representasjon av de virkelige vegene, skilt, tunneller, rekkverk, kummer osv.

## Slide 14: Informasjonsmodeller og ontologier
Information model
  “… a formal description of types of ideas, facts and processes which together form a model of a portion of interest of the real world and which provides an explicit set of interpretation rules.” (Schenck and Wilson, 1994).
  “… a representation of concepts, relationships, constraints, rules, and operations to specify data semantics for a chosen domain of discourse” (Zhao et al., 2011)
≈ Ontology
  “… a set of precise descriptive statements about some part of the world (usually referred to as the domain of interest or the subject matter of the ontology)” (Hitzler et al., 2012)
  “… a common vocabulary for researchers who need to share information in a domain. It includes machine-interpretable definitions of basic concepts in the domain and relations among them”. (Noy and McGuinness, 2001)
Vocabulary
  “terminological dictionary that contains designations and definitions from one or more domains or subjects”.
Formaliserter regler for å forstå data i en kontekst
Definerer konseptene
Implementerer konseptene i et modelleringsspråk
Hva med BIM?

## Slide 15: Informasjonsmodellering
Universe of discourse – interessant del av virkeligheten
Kontekst – i hvilken sammenheng

## Slide 16: Informasjonsmodellering

## Slide 17: From the real world to data set
Hva med BIM?
Notes: When working with data and information, this is where we start. There is a real world out there, and we want to represent it digitally in a way that is fit for our purpose, for example in a map.
In order to do so, we need to define what part of the real world we are interessted in (UoD), and in what context we are studying this UoD. In that context, we define a conceptual model that defines the digital representation, and create data according to that model. For example, we define the class Road, and represent the roads in the picture as objects with polygon geometry. And the same with the poles, fences, buildings and so on.
But for some other context, we may need a different conceptual model of the same UoD, or of a similar but not identical UoD. Therefore, we end up with several conceptual models and several data sets, fit for different contexts, and representing different UoD. In other words: several digital twins.

## Slide 18: Konseptuelle skjemaspråk
EXPRESS
Grafiske
Leksikalske
Uavhengig, maskinlesbart format

## Slide 19: Leksikalske skjemaspråk
EXPRESS

## Slide 20: Grafiske skjemaspråk
EXPRESS-G

## Slide 21: Åpent og lukka syn på verden
Closed World Assumption (CWA)
  The information model is complete in the given context
  Additional or deviating information is invalid
Open World Assumption (OWA)
  The information model presents only what is currently known in the given context
  Additional information extends the model
EXPRESS

## Slide 22: Hvordan klassifiseres virkeligheten?
Dette digitale objektet representerer et fenomen av klassen Rekkverk og kun det.
  Objekter i denne klassen skal ha disse egenskapene, med disse tillatte verdiene…
Dette andre digitale objektet representerer et fenomen av klassen Gjerde
  Objekter i denne klassen skal ha disse egenskapene, med disse tillatte verdiene…
Denne tingen fra virkeligheten er av klassene Rekkverk, Gjerde og Autovern
  Det kan ha noen av disse egenskapene, men også andre
Foto: Silje Drevdal / Statens vegvesen
EXPRESS

## Slide 23: Hva er en svane, hvilken farge har den?
Closed World Assumption (CWA)
  Alle svaner er hvite
Open World Assumption (OWA)
  Denne tingen, klassifisert som en svane, er hvit
  Denne andre tingen, klassifisert som en svane, er svart
From http://www.millennialplanners.com
EXPRESS

## Slide 24: Hva er en and?
Tradisjonell modellering
  Denne tingen er en and
  Den har disse egenskapene:
Description logic
  it looks like a duck, swims like a duck, and quacks like a duck
  it probably is a duck. But not for sure
https://en.wikipedia.org/wiki/Duck_test
EXPRESS

## Slide 26
Allemang, D., Hendler, J.A., Semantic web for the working ontologist : effective modeling in RDFS and OWL. 2nd ed. ed. 2011, Burlington, Mass.: Elsevier.

## Slide 27: Modelldreven arkitektur
Platform Independent Model
Platform Specific Model
Platform Model

## Slide 28: Eksempel: NVDB Rekkverk
https://vegkart.atlas.vegvesen.no/#kartlag:geodata/@299882,6749737,5/hva:~(~(id~5))

## Slide 29: MDA og implementasjonsformater

## Slide 31: Lag og komponenter i IFC
Introduction - IFC4.3.1.0 Documentation (buildingsmart.org)

## Slide 32: Interoperability
Same syntax: UML, EXPRESS, XML, OWL
Same meaning:
What is a guardrail?
ISO/IEC 2382:2015 :“capability to communicate, execute programs, or transfer data among various functional units in a manner that requires the user to have little or no knowledge of the unique characteristics of those units”.
Notes: ISO/IEC 2382:2015 (ISO/IEC JTC 1,
2015) has defined interoperability as “capability to communicate, execute programs, or transfer
data among various functional units in a manner that requires the user to have little or no
knowledge of the unique characteristics of those units”.
The levels of conceptual interoperability has been discussed by many researchers, ranging from no interoperability to full conceptual interoperability. The four core levels are… Additional levels for dynamic and conceptual

## Slide 33: Interoperabilitet
Wang, W., A. Tolk, and W. Wang, The levels of conceptual interoperability model: applying systems engineering principles to M&S. arXiv preprint arXiv:0908.0191, 2009.
Betydning
Språk

## Slide 34: Syntactic interoperability
EXPRESS

## Slide 35: Semantic interoperability
Photo: Silje Drevdal / Statens vegvesen
IFC - IfcRailingType
V.440 – Railing with guardrail
GDF – Safety fixture
What is a guardrail?

## Slide 36: Informasjonsmodellering: Prosessen
Definer domene og bruksområde
Gjenbruk eksisterende modeller
Grunnleggende termer og klasser
Attributter og relasjoner
Restriksjoner og spesifiseringer
Test og valider med instanser
Universe of discourse
Context

## Slide 37: Samspillet mellom aktører
The SEMIC Style Guide for Semantic Engineers :: SEMIC (semiceu.github.io)

## Slide 38: Informasjonsmodellering